FCLWD & SFCSD Operations Department

30Jan15

Substantial  Completion Requirements:

Water & Sewer:

  - All testing has been completed

  - All facilities are to grade and accessible; (roadway facilities minimum road base material, with preventative measures taken to avoid damage to facilities until asphalt is installed.)

  - Record drawings are reviewed and approved.

  - A substantial walk through has been completed by Districts, Developer or Developer Representative, and Contractors Superintendents. It is the Developers or Developers Representatives responsibility to schedule the walk through.

  - Developer is responsible for all facility repairs and maintenance until final close-out is approved and warranty period has expired.

  - Developer is responsible for all facility locates until final close-out is approved.

  - If project is approved for substantial completion, the Developer has six (6) months to complete final close-out. Failure to comply with the completion date will result in suspension of all remaining tap sales, future phases, and/or future projects with Developer until all requirements are satisfied.

  - Developer has submitted written request requirements to the Districts for substantial completion.

Final Acceptance Requirements:

Water & Sewer:

  - All testing has been completed.

  - Tracer wire will be tested and verified by the Districts.

  - All facilities are to final grade and accessible.

  - All facilities will be inspected for final compliance.

  - Record Drawings are reviewed and approved.

  - A final walk through has been completed by Districts, Developer or Developer Representative, and Contractors Superintendants. It is the Developers or Developers Representatives responsibility to schedule the walk through.

  - After the completion of a final walkthrough the Developer has one (1) month to complete all pending items identified. Failure to comply with the completion date will result in suspension of all remaining tap sales, future phases, and/or future projects with Developer until all requirements are satisfied.

  - Developer is responsible for all facility repairs and maintenance until the warranty period has expired.

  - Developer has submitted written request requirements to the Districts for final acceptance.